## Slide 1: Basics of Electrical Circuits
Özkan Karabacak
Oda No:2307
karabacak@itu.edu.tr

## Slide 2: Grading
1 midterm exam | 5 November 2012 | %30
2 short exams | 15 October 2012 | %10
 | 26 November 2012 | %15
Final |  | %45

## Slide 3
References:
L.O. Chua, C.A. Desoer, S.E. Kuh. “Linear and Nonlinear Circuits”
Mc.Graw Hill, 1987, New York ( Sections: 1-8, 12)
Yılmaz Tokad, “ Devre Analizi Dersleri” Kısım I, Çağlayan
Kitabevi, 1986.
Cevdet Acar, “Elektrik Devrelerinin Analizi” İ.T.Ü. Yayınları,
1995.

## Slide 4
Circuit Theory
Goal: to predict the electrical behaviour of physical circuits
Physical circuit: interconnections of (physical) electric devices
Why(When) do we need to predict the electrical behaviour?
..........................................................................
..........................................................................
(Electrical) circuit: model of physical circuit
Domain of application: large-scale integrated circuits (fingernail size)
telecommunication and power circuits (continent size)
voltage μV MV
current pA MA
frequency 0 Hz 1GHz
power 10-14 W 109 W

## Slide 5
A physical circuit
Main unit of a random number generator: chaotic oscillators
Ahmet Şamil Demirkol, Serdar Özoğuz, Vedat Tavas

## Slide 6
... and its model
I0+IY
IB
2(I0+IX)
I0+IX
C1
2KI0
comparator
I0(1+ε)
ICout
VDD/2
I0+IZ
C3
I0
C2
I0+IY
kI0
MC1
MC2
MA
MB
Me1
Me2

## Slide 7
Oscilloscope images

## Slide 8
How should we start building a theory?
undefined quantities
axioms
What else do we need?
for new quantities: definitions
for new results: theorems

## Slide 9
Electrical Circuit Theory
undefined quantities
current voltage
i(t) [A] v(t) [V]
An electrical circuit
A
V
+
_
+
_

## Slide 10
Be careful in directions!
The directions of currents and voltages in a circuit usually changes. Therefore, there is no (true) specific direction that can be assigned to these.
Nevertheless, we need directions before we start analysis. We proceed as follows: We choose directions arbitrarily. If after the analysis the value of a current is estimated as positive, then the actual direction of the current is the same as the (reference) direction you chose. If it is negative, then the actual direction is the opposite of the direction you chose.
i3(t0)=(+/-)2A means current at time t0 flows (into/out of) the device from terminal 3 in (b).
vk(t1)=(+/-)25V means that, at time t1, the electric potential of the terminal k in (c) is 25V (larger/smaller) than the electric potential of terminal n.
reference direciton
+
sign
=
actual
direction

## Slide 11
Axioms
1. Lumped circuit:
A physical circuit can be consider as lumped if its physical size () is negligble compared to the wavelength () of the signal. In other words,
, where is the frequency and is the velocity of the signal.
What is the velocity of electric?
..........................

## Slide 12
Axioms
2. Kirchhoff’s Voltage Law (KVL)
1824-1887
Given any connected, lumped circuit having n nodes, choose one of these nodes as a reference node.
Define n-1 node-to-reference voltages as shown in the figure below.
. . .
. . .
1
2
3
k
n-1
n
en=0
+
_
+
_
+
_
+
+
_
_
e1
e2
e3
ek
en-1
Denote the voltage difference between node k and node j by vkj .
Vkn-1

## Slide 13
Kirchhoff’s Voltage Law (KVL) in terms of node voltages
For all lumped connected circuits, for all choices of reference node, for all times t, for all pairs of nodes k and j,
For all lumped connected circuits, for all closed node sequences, for all times t, the algebraic sum of all node-to-node vol
Kirchhoff’s Voltage Law (KVL) for closed node sequences
Theorem:
KVL in terms of node voltages KVL for closed node sequences

## Slide 14
Example
Write the equations obtained from KVL in terms of node voltages.
Choose three closed node sequences and write three equations using KCL for closed node sequences.
1
2
3
4
5
6
7
8
L.O. Chua, C.A. Desoer, S.E. Kuh. “Linear and Nonlinear Circuits”, Mc.Graw Hill, 1987, New York

## Slide 15
3. Kirchhoff’s Current Law (KCL)
Gaussian surface :
+
_
a closed surface. We choose such a surface such that it cuts only the connecting wires between the circuit elements but not the elements themselves or the nodes.

## Slide 16
For all lumped circuits, for all Gaussian surfaces, for all times t, the algebraic sum of all the currents leaving the Gaussian surface at time t is equal to zero.
Kirchhoff’s Current Law (KCL) for Gaussian surfaces
Kirchhoff’s Current Law (KCL) for nodes
For all lumped circuits, for all times t, the algebraic sum of the currents leaving any node at time t is equal to zero.
Theorem:
KCL for Gaussian surfaces KCL for nodes

## Slide 17
Example
Choose three Gaussian surfaces and write three equations using KCL for these Gaussian surfaces.
Write the equations obtained from KCL for nodes.
1
2
3
4
5
6
7
8
L.O. Chua, C.A. Desoer, S.E. Kuh. “Linear and Nonlinear Circuits”, Mc.Graw Hill, 1987, New York

## Slide 18
Finally,
KVL and KCL equations can be obtained only for lumped circuits,
does not depend on the elements themselves,
does depend only on the connection structure
of the elements
are linear, algebraic, homogeneous equations
with coefficients 1,-1 or 0.